# Rootfs notes
## Rootfs in FLASH (UBIFS)
The easiest way to generate UBIFS image is by setting BR2_TARGET_ROOTFS_UBIFS to y in the buildroot config. Buildroot will also need the following file system parameters, that can be queried with mtdinfo tool:
- BR2_TARGET_ROOTFS_UBIFS_LEBSIZE: logical erase block (LEB) size (130944 for this device)
- BR2_TARGET_ROOTFS_UBIFS_MINIOSIZE: minimum I/O unit size (1 for this device)
- BR2_TARGET_ROOTFS_UBIFS_MAXLEBCNT: maximum logical eraseblock count (this device has 768, 764 are usable, as reported by ubiattach).
# mtdinfo -a -u
Count of MTD devices: 4
Present MTD devices: mtd0, mtd1, mtd2, mtd3
Sysfs interface supported: yes
mtd0
Name: data
Type: nor
Eraseblock size: 131072 bytes, 128.0 KiB
Amount of eraseblocks: 768 (100663296 bytes, 96.0 MiB)
Minimum input/output unit size: 1 byte
Sub-page size: 1 byte
Character device major/minor: 90:0
Bad blocks are allowed: false
Device is writable: true
Default UBI VID header offset: 64
Default UBI data offset: 128
Default UBI LEB size: 130944 bytes, 127.9 KiB
Maximum UBI volumes count: 128
To format FLASH partition and put UBIFS image into it the following command sequence may be used:
run ubiformat:
# ubiformat /dev/mtd0
ubiformat: mtd0 (nor), size 100663296 bytes (96.0 MiB), 768 eraseblocks of 131072 bytes (128.0 KiB), min. I/O size 1 bytes
libscan: scanning eraseblock 767 -- 100 % complete
ubiformat: 768 eraseblocks have valid erase counter, mean value is 2
ubiformat: formatting eraseblock 767 -- 100 % complete
attach formatted device to UBI (this will create /dev/ubi0 device):
# ubiattach -p /dev/mtd0
UBI device number 0, total 768 LEBs (100564992 bytes, 95.9 MiB), available 764 LEBs (100041216 bytes, 95.4 MiB), LEB size 130944 bytes (127.9 KiB)
create UBI volumes on formatted device (this will create /dev/ubi0_0 device, AKA ubi0:rootfs):
# ubimkvol /dev/ubi0 -m -N rootfs
Set volume size to 100041216
Volume ID 0, size 764 LEBs (100041216 bytes, 95.4 MiB), LEB size 130944 bytes (127.9 KiB), dynamic, name "rootfs", alignment 1
- put UBI rootfs image so that xtensa linux could access it (in this example kernel is booted with NFS root and UBI image goes to /mnt/rootfs.ubifs)
- run ubiupdatevol to copy file system image to the specific UBI volume:
# ubiupdatevol /dev/ubi0_0 /mnt/rootfs.ubifs
now the volume may be mounted:
# mount -t ubifs /dev/ubi0_0 /mnt
to use that volume as rootfs add the following parameters to the kernel command line (note that 0 in the 'ubi.mtd=0' is the number of mtd partition to bind to ubi0, and 'rootfs' in the ubi0:rootfs below is the volume name):
ubi.mtd=0 root=ubi0:rootfs rootfstype=ubifs
### Further reading:
- http://www.linux-mtd.infradead.org/doc/ubifs.html
- http://www.linux-mtd.infradead.org/faq/ubifs.html
- https://www.kernel.org/doc/Documentation/filesystems/ubifs.txt