# Booting xtensa linux on qemu
## Issues
### wrong address generated for jump in kernel_exception_return
arch/xtensa/kernel/entry.S:777
        movi a0, 1f + (0x40000000 - 0xC0000000) # Calculate Return address for "1f" and store in a0
        rsil a2, XCHAL_EXCM_LEVEL # FIXME: again, only do this if PS.INTLEVEL <= EXCM_LEVEL
        retw # rotate back by 4 registers, possibly with underflow
        # Back out our _entry Frame above...
        # ... We return here from above retw.
1: mov a1, a5 # our a1 became a5 at the above _entry, a1 = a5
Assembled it looks like this:
0010 ffffff3f 00000000 000000c0 05030080
...
        1c: R_XTENSA_32 .text
...
2fd: 000001 l32r a0, fffc0300 <ret_from_fork+0xfffbf858>
        2fd: R_XTENSA_SLOT0_OP .literal+0x1c
300: 006320 rsil a2, 3
303: f01d retw.n
305: 051d mov.n a1, a5
Linked vmlinux looks like this (broken, word at d000357c should be 2d3d0050):
d0003570 ffffff3f e83b00d0 000000c0 cd3c0050
...
d0003d25: fe1501 l32r a0, d000357c <T$339+0x68>
d0003d28: 006320 rsil a2, 3
d0003d2b: f01d retw.n
d0003d2d: 051d mov.n a1, a5